CACTI
Presented By Atishay Jain
NOV 19 2018

---
Introduction
Introduction
- CACTI  is  a  memory  modeling  tool  that  currently  comes  from  HP Labs.
- CACTI  is  a  tool  that  allows  you  to  explore  the  performance,  area,  and  power  impacts  of cache memories.
- CACTI can correctly evaluate the power, area, and timing overhead of adding the power management units, including the penalties of wakeup latency and wakeup energy.
- Using CACTI 6.5, cache memory can be simulated according to the requirements.

---
Download CACTI
Install CACTI 6.5
Installation issue fix:
https://askubuntu.com/questions/709893/14-04-01-32-bit-missing-g-64-bit-include-files-when-cross-compiling
Documentation:
http://www.hpl.hp.com/research/cacti/
http://www.hpl.hp.com/techreports/Compaq-DEC/WRL-93-5.html
http://www.hpl.hp.com/techreports/2009/HPL-2009-85.html
CACTI 4.0
http://www.hpl.hp.com/techreports/2006/HPL-2006-86.pdf

---
Working Of Cacti
- INPUT Configuration File (cache.cfg)-
  Input Parameter
  1.Cache Size
  2.Set Associativity
  3.Number of read write port
  4.Technology node (nm)
  5.Operating temprature
  6.Type of Cache Transistor
  7.Core Count
  8.Design Objective
- Output result in terminal-
  1.Access time
  2.Dynamic Energy
  3.Leakage Power
  4.Area for tag bits and data bits

---
Command to run CACTI
./cacti -infile cache.cfg
Output can be stored in a file using the command
./cacti -infile cache.cfg>out1.txt

---
Usage
Usage
- Prior versions of CACTI take cache parameters such as cache size, block size, associativity, and technology as command line arguments. CACTI 6.0 also employs a configuration file (cache.cfg) to enable user to describe the cache parameters in much greater detail
- Other non-standard parameters that can be specified in the cache.cfg file include
    • No. of read ports, write ports, read-write ports in a cache
      • H-tree bus width
    •Operating temperature (which is used for calculating the cache leakage value),

---
Cacti Terminology
Cacti Terminology
- Bank –A cache may split in multiple banks and these banks can be accessed simultaneously.
- Sub Array-Data and tag are divide into number of sub arrays to reduce the delay due to wordline and bitline.
- Mat-A group four sub array that share a common central predecoder. CACTI’s exhaustive search starts from atleast one mat.

---
Understanding 	Configuration Files
Understanding	Configuration Files
1.Size (byte)-It must be a power of 2-If the value is to big then it can end up showing error.
2.Associativity-It can be 0 or some power of 2
   0 means fully associative
   1 means direct associative
   Other powers if two are the number of ways in the set
3.Technology (nm)- It is the process used for the fabrication in nano meter.

---
4.There are multiple transistor types that are available
    1.itrs-hp-High Performance
    2.itrs-lstp-low standby power(leakage power)
    3.itrs-lop-low operating power(dynamic power)
    4.lp-dram-This means logic cell is made up of dram transistor.(using dram)
   The choice of cell type varies – for small memories hp is good but for large memory lstp is prefered.

---
5.Tag size –It can be specified as default which work fine for basic circuit , but for modelling something more real tag bits must be choosen with care.
6.Three Access mode
   1.Fast-data and tag access in parallel and the whole set is broadcast over the H –tree.
   2.Sequential -Tag access happens first then data bits are accessed.
   3.Normal-data and tag bits are access in parallel but the tags are used to select which way to be delivered to the H-tree.

---
7.Differential wire signalling are
   1.Lowswing-It uses less energy to charge and discharge wire capacitance but require more sensitive sense amplifier.
   2.Fullswing-Wire uses simple sense amplifier but require more energy to charge or discharge the capacitor.
   3.default-Cacti will search for the best option and report the best result.
    In general big memories are slow and smaller memory so a common strategy is to build a larger memory out of the smaller number of storage array called mats.

---
8.Wire pitch inside or outside of the mats has influences delay.
   1.Global – Used to connect long interconnects between the blocks, including power, ground and clocks..
    2.Semi global- Used to connect devices within a block

---
CACTI-IO
CACTI-IO
- CACTI-IO provides IO power numbers for Read, Write, Idle (only clock active) and Sleep modes that can easily be integrated into a system simulator
- Enable co-optimization of off-chip and on-chip power and performance, especially for new off-chip topologies.
- When designing new off-chip configurations, many new tradeoffs arise based on the choice of off-chip interconnect, termination type, number of fanouts, operating frequency and interface type (serial vs. parallel)
- Provides facility of Power gating at various levels.

---
Trade off Analysis
Trade off Analysis
- The new version allows default cost function to evaluate cache organization.
- The weight for each term (W acc time, Wdyn power, Wleak power, Wcycle time, Warea) indicates the relative importance of each term.
     :-weight 100 20 20 10 10
- In addition, the following default line in the input parameters s to deviate from the optimal set of metrics
  : -deviate 1000 1000 1000 1000 1000
- It also takes either ED or ED square as input to its cost function to determine a cache organization that has best energy-delay or energy – delay product

---
Conclusion
Conclusion
- CACTI 6.5 is a good to analyze and understand the various trade off between area,delay and power.
- CACTI tool gives a detailed description of various parameters.
- Helps in understanding Cache in a better way.

---
REFRENCES
1.http://www.hpl.hp.com/research/cacti/
2.http://www.hpl.hp.com/techreports/2009/HPL-2009-85.html
3.CACTI-IO Technical Report